## Slide 1
Faster STORM using compressed sensing
Lei Zhu et al.
Nature method. (2012.04)
Presenter : Eunseok Jung
GIST, Dept. of Mechatronics , Bioscopy Lab.
Notes: Good afternoon everyone~
First of all, thank you for attending my MS defense presentation.
My name is Younghak Shin
Im a member of INFONET lab. at GIST
The title of my thesis is this

## Slide 2: Background
STORM (Stochastic optical reconstruction microscopy)
STORM is a super-resolution optical microscopy
technique based on stochastic switching of single-molecule fluorescence signal.
STORM utilizes fluorescent probes that can switch between fluorescent
and dark states so that in every snapshot, only a small, optically resolvable fraction
of the fluorophores is detected.
This enables determining their positions with high precision from the center positions
of the fluorescent spots.
Cited form : http://huanglab.ucsf.edu

## Slide 3
Matrix(A)
Optic system - LTI
Original Image(X)
Microscope image
-Blurred picture
Fluorephore(Yes)
Fluorephore(No)
From : http://www.ruf.rice.edu/
Notes: [그림 ] 연구 내용 개념도 (2). Compressed sensing을 이용한 시스템 성능 개선

## Slide 4
Matrix(A)
Optic system - LTI
Original Image(X)
Microscope image
-Blurred picture
Fluorephore(Yes)
Fluorephore(No)
From : http://www.ruf.rice.edu/
Notes: [그림 ] 연구 내용 개념도 (2). Compressed sensing을 이용한 시스템 성능 개선

## Slide 5: Background
Point spread function(PSF)
The point spread function (PSF) describes the response of an imaging system to a point source or point object.
A more general term for the PSF is a system's impulse response, the PSF being the impulse response of a focused optical system.
From : http://en.wikipedia.org

## Slide 6: Introduction & Motivation
Super resolution microscope overcome traditional optical
microscope limit.(According to Abbe’s theory : )
The super resolution microscope and fluorescence technique make spatial resolution closer to the molecular scale.(Approximately : 30nm)
Now we can see a ten nanometer scale cell structure.
From : Imaging Intracellular Fluorescent Proteins at Nanometer Resolution, E. Beitzig, science, 2006

## Slide 7: Introduction & Motivation
Benefit of compressed sensing in fluorescence imaging.
C.S.
Algorithm
High resolution
result
Microsocpe image
32*32 pixel
Reconstruction
256*256 pixel
Conventional fluorescence image
Compressed sensing image

## Slide 8: Oversampling
For increasing spatial resolution, the author used grid method.
According to the nyquist theorem, we need 2 times more sampling for reconstruct singal. In here, 21nm*2=42nm.
Finally, the reconstruction image can get a 42nm spatial resolution.
1 : 64

## Slide 9: Measurement matrix (1)
Measure the PSF of optic system.
Fit the Gaussian function.
Optic system is LTI system.

## Slide 10: Measurement matrix (2)
A
x
(M<N)
A = Measurement matrix
x = Reconstruct image
b

## Slide 11
A
x
(M<N)
A = Measurement matrix
x = Reconstruct image
b
- Measurement matrix A
Measurement matrix (3)

## Slide 12: Measurement matrix (4)
A
x
(M<N)
A = Measurement matrix
x = Reconstruct image
b
- Measurement matrix A

## Slide 13: Measurement matrix (5)
A
x
(M<N)
A = Measurement matrix
x = Reconstruct image
b
64 : 1

## Slide 14
Matrix(A)
Optic system - LTI
Original Image(X)
Microscope image
-Blurred picture
Fluorephore(Yes)
Fluorephore(No)
From : http://www.ruf.rice.edu/
Notes: [그림 ] 연구 내용 개념도 (2). Compressed sensing을 이용한 시스템 성능 개선

## Slide 15: Reconstruction
The matrix A is determined by the point-spread function (PSF)
of the imaging system.
The i th column of A corresponds to the acquired raw image
if only one molecule emits fluoroscopic photons at the position index i of x.
The weight vector c is to account for the difference of the total contribution
to the camera image from one fluorescent molecule at different locations.
The value of the i th element of c equals the summation of the i th column of A.
The minimization term cTx is equivalent to a weighted L1 norm of x
because x is non-negative.

## Slide 16: Reconstruction
CVX converts the above problem to an SOCP (Second-order cone programming), and solves it.

## Slide 17: Results
Scale bar : 300nm
FOV : 4um*4um
Pixel : 32*32
Scale bar : 300nm
FOV : 4um*4um
Pixel : 256*256
The pixel size of 166nm, the 21nm grid size should be able to support a final image resolution of 42nm.
C.S.
Algorithm

## Slide 18: Results
Conventional fitting

## Slide 19: Results

## Slide 20: Results

## Slide 21: Data Analysis and Discussions
The red-cross is the reconstructed image using compressed sensing
The white one is fluorescence position (original image).
The maximum difference between two positions is 60nm.
Scale bar is 300nm.

## Slide 22: Conclusions
Conclusion
This journal has potential benefit. It was first step of compressed sensing with super resolution microscope.
It had not been impossible to taking a living cell image without compressed sensing.
Now, it could be done with compressed sensing.
The author spent 3sec for taking living cell photo. And they get a same result when they spent over 30sec. They decrease experiment time 10times more.
According to this, now we can get a living cell image.

## Slide 23: Improvement
Algorithm
If we make measurement matrix A using difference method, we can decrease error and also increase spatial resolution.
The other reconstruction method, instead of SOCP, can decrease error.
Hard ware
The author used EM-CCD camera, it is very expensive detect device.
But if we can make same result using cheap detect device like a sCMOS or
CMOS, the system cost is more cheaper than before.

## Slide 24
Thank you