## Slide 1
M=40, N= 405
Conventional limit = 10 nm
Spectrum : Mercury lamp with 7 spectral components
Least separation between spectral components : 2.106 nm
Achieved resolution = 0 .99 nm
Random Transmittance Based Filter Array Spectrometers:
Sparse Spectrum Recovery And Resolution Improvement
Oliver James, Woong-Bi Lee, and Heung-No Lee, Gwangju Institute of Science and Technology, South Korea
Each filter is implemented using thin-film technology
In thin-film filters,
Transmittance = f ( No. of layers, thickness, refractive index )
We randomly vary thickness of each layer to obtain random transmittance
4. Implementation Approach
2. Spectrometer Schematic
5. Results
Resolution limit is decided by
No. of filters in the filter array
Shape of transmittance function (TF)
Spectrometers reveal fine details about the various spectral components of the incident light
In recent years, resolution of spectrometers is increased by the use of L1-norm based algorithms
Performance of L1-based algorithms depend on the transmittance of the filters in the filter-array
1. Background
What are good transmittance functions (TF) for improving resolution?
Raw spectrum model: y = DGs + w
  TFs form the rows of the transmittance matrix
  Traditionally desired TF shape is ideal brick-wall
For L1-based spectrometers, random transmittances are best!
Properties of Random transmittances
  Dirac-delta like Auto-Covariance (AC)
  Zero Cross-Covariance (CC) between a pair of TFs
3. Design Approach
Transmittance matrix
Gaussian
Kernel
=
+
Filters are analog!
Oliver James : oliver@gist.ac.kr
Heung-No Lee: heungno@gist.ac.kr
Contact
Raw spectrum
Sparse spectrum
Noise
N x 1
M x 1
M < N
Fig. 4. (a) Original sparse
spectrum of the mercury lamp.
(b) Estimated sparse
spectrum by using TFs in [5].
(c) Estimated sparse spectrum
by thin-film-based random TFs.
Fig. 1. Schematic of the proposed spectrometer
Fig. 2. Thin-film filter
Random TFs are designed to acquire holistic information, rather than the localized information
Our random TFs bring a shift in the design paradigm resulting in an order-of-magnitude resolution improvement
6. Conclusions
Fig 3. (a) Random transmittances produced by the thin-film method.
(b) AC of Filter-5. (c) CC between Filter-5 and Filter-20.
Prototype
10-fold resolution improvement